DESIGNING OF ANALOG AND DIGITAL FORMING FILTERS

George Kuyumchev

Saint-Petersburg State University of Aerospace Instrumentation

Saint-Petersburg, Russia

- INTRODUCTION

This paper describes the methods of designing of analogue and digital forming filters on the set spectral density or correlation function of target signals.

Forming filters are the devices intended for formation from white noise (is more rare colored) random process with the set statistical characteristics. Linear forming filters are most often applied, normal white noise is used as entrance signals. Random normal processes with demanded statistical characteristics – spectral density or correlation function will be output signals of such filters.

Forming filters have found wide application at mathematical modeling of radio-electronic systems on the COMPUTER where the algorithm of work of the filter is used for imitation of fluctuations of entrance signals of projected system. Besides, forming filters are used as model of entrance process at synthesis of filters Kalmana-Bjusi, and also for designing of simulators of the information and stirring signals used at seminatural, laboratory and field tests of radio-electronic equipment.

For synthesis of algorithm of work of the forming filter it is necessary to set or spectral density of a output signal of the filter, or its correlation function. From the theoretical point of view it is indifferent what to set, as these two characteristics of random process are connected by univalent transformation of Wiener-Hinchina, that is, knowing one of them, it is possible to find another. However, if the spectral density or correlation function has been received as a result of experiment at the task of statistical characteristics of process it is desirable to use that, from them, which has been received directly, as transformation of an experimental curve can entail increase in an error of the initial data used at synthesis of forming filters.

This work describes synthesis of linear forming filters, on which input normal white noise with a zero average and an individual dispersion moves, is considered. The offered technique with little changes can be generalized and on synthesis of nonlinear filters [2]. Besides restrictions by linear algorithms, restrictions on spectral density and correlation functions are entered, which are considered only such which correspond to Markov processes. Restriction by Markov processes is not essential for developers of equipment as any random process with sufficient accuracy for practice can be approximated by n-dimensional Markov process with corresponding increase n. Restriction by Markov processes is conveniently from the point of view of their modeling on the COMPUTER as it allows to receive exact algorithms of modeling at final number of differential equation.

- SYNTHESIS OF ANALOGUE FORMING FILTERS

Initial data for synthesis of analogue forming filters (AFF) are spectral density  or correlative function  of output signal. Two continuous casual processes  and  are connected by mutual transformation Furie.

Synthesis AFF on the set spectral density.

The spectral density of stationary Markov process is represented in the form of fractionally- rational function of frequency [1]

where  and  some polynoms from . Random process g(t) on exit AFF  can be treated as an output signal of the filter with the module of frequency transfer function , on which input white noise  operates. It is proved, that fractionally-rational  supposes factorization [1]

where function  can be chosen so that its zero and  poles would be  laid in the top half-plane, and zero and a pole  – in the bottom half-plane of quantity  ((in the left and right  half-plane  of size ).

Then the ratio

where , defines frequency transfer function of some steady linear filter which is the required forming filter. The linear differential equation match to this filter.

For realization AFF on the COMPUTER use the equation (2,4) for its solution it is necessary to choose any numerical method providing the set error of result. The subroutine of the solution of the equation (2.4) defines the mathematical model AFF, realized on the COMPUTER.

At realization AFF on the COMPUTER or in the form of the separate analogue block it is more convenient to use the equation (2.3) which, after division of both parts on  will transform to a form

It is necessary to notice, that the operator                 corresponds to the ideal integrator, for real integrators transfer function will be equal , where  the factor of transfer, having physical dimension inverse dimension of time.

Synthesis AFF on the set correlation function.

While tasking correlation function , it is possible, as it was specified above, to pass to spectral density , and then make synthesis on . As we were limited by normal Markov  processes, that is, excepting a case of a multiple root of a characteristic polynom of the differential equation  defining Markov process, we will receive, that  is possible to present like the weight sum of curves of a kind

Thus the sum of weighting coefficients should be equal to unit. Then for transition from  to, it is necessary to replace each function from with its image on Furie. Originals  and their Furie-images  are resulted in tab. 2.1.

Tab 2.1

| The original | The image |
| --- | --- |
|  | 1 |

It is necessary to notice, that synthesis AFF on set  can be much easier then synthesis on set, that is connected with difficulty factorization  at the big dimension n. At the same time at synthesis on set , presented in the form of the weight sum of curves of type (2.5) ,at positivity of weight factors, output signal AFF can be treated as the weight sum of output signals private AFF, each of which is raised by the white noise.

Really, let  and

Output signal AFF we will present as

where  an output signal of i- th AFF, defined by the correlation function.

Then

where  mutual correlation function of output signals by - th and К- Th private AFF. If entrance processes private AFF are statistically independent,  for all possible combinations  and . In this case

where . Private AFF contain no more than two integrators, despite necessity of a multidimensional entrance signal, it can appear more comprehensible on accuracy of reproduction of statistical characteristics of output process, as two-multiple integration on analogue integrators is carried out much more precisely, than n-fold.

In summary we will give an example synthesis AFF.

Example 2.1.

Let correlation function is equal

Synthesis on .

where

Synthesis on

Private -th AFF has spectral density of an output signal

From which directly receive frequency transfer function of the filter

where

- SYNTHESIS OF DIGITAL FORMING FILTERS

For the purposes of digital forming filters (DFF) we will consider, that signal digitization is made with period Т, and digit capacity of digital elements on which is realized DFF, is so great, that signal quantization on level can not be considered. This assumption practically is always carried out at realization DFF on the COMPUTER, at use of modern microprocessor complete sets Bis always it is possible to increase their digit capacity. Therefore such restriction is not too strong for the developer  of equipment. Besides, the effect of quantization can be always considered by mathematical modeling of received structure DFF, for the purpose of getting more exact statistical characteristics of an output signal of the filter, on which it is possible to modify the synthesized structure.

As input signal DFF we will use discrete normal white noise - trellised casual process , each readout of which is a normal random variable with a zero average and an single dispersion. Output signal DFF – trellised casual process   with the set statistical characteristics spectral density or correlation function. We will consider only normalized correlation functions which represent trellised functions from the integer argument, defined by expression  where М – a sign on mathematical averaging. For getting  a preset value of a dispersion of a signal such DFF it is necessary to increase its output signal on size equal to a square root from the set dispersion. As to spectral density of trellised casual process use three its kinds.

The first kind – spectral density as function of circular frequency  is defined through bilateral transformation Furie from

Thus  is inverse transformation Furie, calculated on an interval of periodicity  equal

The second kind - spectral density as function  is defined bilateral  – transformation

where  – -transformation (unilateral) , in penultimate equality is used property of parity . As follows from (3.1) and (3.3) (3.1) и (3.3)  it turns out simple substitution  from .

The third kind - spectral density as pseudo-frequency function  is defined from  after substitution

This transformation allows to observe only one period, which is stretched on all axis of pseudo-frequency. Spectral density  is analogue of spectral density  an analogue signal. The formula of the reference for  turns out corresponding substitution from (3.4) to (3.1)

Any digital filter is completely defined by the difference equation or discrete transfer function. As we are limited by Markov processes (in this case Markov chains) that difference equation DFF will contain final number of members, and transfer function will be fractionally rational function  .

Synthesis DFF on the set spectral density.

Any type of spectral density ,  or  can be set. However in the initial spectral density, subjected factorization (similar case AFF), is , therefore at task  or  at first it is necessary to pass  to  by substitution

After that we receive  in the form of fractionally rational function from   .

which also factorize as well as , and function  such, that its zero and poles would be laid in the bottom of  half plane of size  (in the left half plane of size . Then, as well as earlier, transfer function of the forming filter is defined by .

If DFF is used for generation of an entrance signal of radio-electronic system, then 
 is possible to present as .

That physically means a delay of an output signal of the filter on  steps, if DFF is used in filter Kalmana-Bjusi it is impossible to enter a delay. This feature DFF allows to represent  in the kind most convenient for realization.

To the digital filter with frequency transfer function   match transfer function , which turns out from  by means of permutation

Then  is represented in the form of fractionally rational function from

multiplication  on

corresponds to multiplication   on , therefore for DFF   is possible to present  as

where . To the digital filter with transfer function  corresponds difference equation

Synthesis DFF on correlation function.

While tasking correlation function  it is possible to pass to, and then to, then the technique of synthesis DFF on the set spectral density is applied. The most widespread  and their bilateral - transformations are resulted in tab. 3.1.

Table 3.1

| The original | The image |
| --- | --- |

As well as for AFF it is possible to treat target signal DFF as the sum of target signals of private forming filters (only at positivity of weight factors).

Other approach to construction DFF which uses only correlation function, is possible also. This approach is stated in [3], its consideration is beyond this work.

- CONCLUSION

This paper describes classical methods of synthesis of digital and analogue forming filters. At realization of these filters on the Computer it is more preferable the methods of the synthesis using set correlation function, and at realization of filters in the form of separate analogue devices (or on the analogue COMPUTER) it is more convenient to use spectral characteristics of modeled signals.

REFERENCES

- Бесекерский В.А. Цифровые автоматические системы.-Наука.М.,1976,с 43…48,155…170,273…278,.324…341.

- Оводенко А.А., Шепета А.П. Проектирование робастных локационных устройств.-Учебное пособие.ЛИАП-ЛЕТИ.Л.,1983,с.82…85.

- Shepeta D.A. Synthesis of the Non-linear Forming Filters for Radiolocation Systems Input Signals Modelling. Abstract. ISA Conference St.-Peterbyrg 2000.

# Text boxes

(2.2)

(2.1)

(2.3)

(3.4)

(3.3)

(2.4)

(3.2)

(3.1)

(2.5)